## Slide 1: Smart Autonomous Multi-Mode Robot Using Arduino
EMBEDDED SYSTEM DESIGN AND IoT PROJECT
Obstacle avoidance, Bluetooth and voice control on one Arduino UNO
R. Samshritha | 2520030045
G. Lasya Sai | 2520030538
P. Asritha | 2520030592
P. Bindhu Madhavi | 2520030077
G. Laxmisri | 2520030264
Supervisor: Dr. V. Ravi Kumar | B.Tech II Year, AY 2026-27 Odd Sem
Dept. of Computer Science Engineering, KLEF Bachupally, Hyderabad | October 2026
UNO
7.4 V

## Slide 2: Abstract
Many low-cost robot cars offer only one control mode. This project builds a four-wheeled robot on an Arduino UNO that combines three.
An HC-SR04 sensor on an SG90 servo scans for obstacles, an HC-05 Bluetooth module takes smartphone commands, and an L298N driver powers four BO gear motors from two 18650 cells.
Each mode is its own function, chosen with a switch, so no code re-upload is needed.
Applications: warehouses, surveillance, education, assistive robots
3
operating modes
4
BO gear motors, 60 RPM
12 cm
obstacle stop distance
7.4 V
2 x 18650 Li-ion pack

## Slide 3: Block Diagram
Smartphone App
(buttons / voice)
HC-05 Bluetooth
Mode Switches
SW1, SW2, SW3
Arduino UNO
(ATmega328P)
HC-SR04
Ultrasonic
SG90 Servo
(scanner)
2 x 18650 (7.4 V)
+ slide switch
L298N
Motor Driver
Left motors
M1, M2
Right motors
M3, M4
Bluetooth
UART D0/D1
D2-D4
A0/A1
A2
D8-D11
7.4 V
Power path
Signal / control path

## Slide 4: Components Used
Component | Qty | Role in the project
Arduino UNO (ATmega328P) | 1 | Main controller running the firmware
L298N motor driver | 1 | Drives four DC motors as left and right pairs
HC-SR04 ultrasonic sensor | 1 | Measures distance to obstacles
HC-05 Bluetooth module | 1 | Wireless link to the smartphone
SG90 micro servo | 1 | Rotates the sensor left and right
60 RPM BO gear motor + wheel | 4 | Four-wheel drive
18650 Li-ion cell, dual holder | 2 | 7.4 V supply (2 x 3.7 V in series)
Mode switches SW1-SW3 | 3 | Select obstacle, Bluetooth or voice mode
Also used: slide power switch, jumper wires, foam-board chassis

## Slide 5: Circuit and Pin Allocation
Device | Arduino pin | Notes
HC-SR04 Trig / Echo | A1 / A0 | 10 us pulse; pulseIn, 30 ms time-out
SG90 servo signal | A2 | 20 (right), 103 (centre), 180 (left)
L298N IN1, IN2 | D8, D9 | Left motors M1, M2
L298N IN3, IN4 | D10, D11 | Right motors M3, M4
HC-05 TXD / RXD | D0 / D1 | 9600 baud; unplug while uploading
Switch SW1 | D2 | Obstacle avoidance (ON = LOW)
Switch SW2 | D3 | Bluetooth control (ON = LOW)
Switch SW3 | D4 | Voice control (ON = LOW)
Full-speed drive
ENA and ENB stay on their jumpers, so both channels are always enabled and the motors run at full supply voltage.
Software speed control needs ENA/ENB on PWM pins (future work).

## Slide 6: Multi-Mode Operation
SW1 / D2
Obstacle Avoidance
Sensor scans ahead; the robot stops, looks both ways and turns toward the freer side.
SW2 / D3
Bluetooth Control
Phone buttons send F, B, L, R or S; the last command stays active.
SW3 / D4
Voice Control
Phone turns speech into symbols; turns are checked for free space first.
How the mode is chosen: switches use INPUT_PULLUP, so ON = LOW. loop() runs Obstacle(), Bluetoothcontrol() or voicecontrol() for the switch that is ON. Only one switch should be ON at a time, and no re-upload is needed to change mode.

## Slide 7: Working: Obstacle Avoidance
Read distance
(HC-SR04)
distance <= 12 cm ?
Move forward
No
Yes
Stop, reverse
100 ms
Scan left 180
and right 20
Compare L
and R
L < R
Turn right
500 ms
L > R
Turn left
500 ms
L = R
Reverse
500 ms
Then the loop resumes. If no echo arrives within 30 ms, the distance is taken as 400 cm.

## Slide 8: Working: Bluetooth and Voice Control
Bluetooth (HC-05)
One character per button press, 9600 baud
F
Forward
B
Backward
L
Turn left
R
Turn right
S
Stop
Voice (phone app)
Speech converted to a symbol by the app
^
Forward
-
Backward
<
Left, only if 10 cm free
>
Right, only if 10 cm free
*
Stop
Tank turning: one side runs backward while the other runs forward, set through IN1-IN4. The last Bluetooth command stays active until a new one arrives.

## Slide 9: Results and Discussion
Chart: Sensor accuracy: tape vs robot
| 5 | 10 | 20 | 50 | 100
Actual (cm) | 5 | 10 | 20 | 50 | 100
Measured (cm) | 5 | 10 | 19 | 49 | 98
12 / 12
functional tests passed
2 cm
maximum sensor error (2% at 100 cm)
12 cm
stop threshold, well above the error
Operation slowed when the battery was low.

## Slide 10: Limitations and Future Work
Limitations
No wheel encoders, so speed and distance are not measured
Single narrow-beam sensor can miss side objects
Bluetooth range about 10 m, no cloud link
ENA/ENB jumpers: full speed only
Future Work
ESP32 or NodeMCU for Wi-Fi and cloud (Blynk, MQTT)
PWM on ENA/ENB for software speed control
Command time-out when Bluetooth drops
Encoders, IMU and a camera for navigation

## Slide 11: Conclusion
A low-cost Arduino UNO robot can combine autonomous and remote operation in a single, reproducible design.
1
Built
Four-wheel robot with scanning sensor, L298N drive and HC-05 link.
2
Tested
12 tests passed; obstacle at 12 cm detected and avoided.
3
Extensible
Modular firmware ready for Wi-Fi, PWM speed and encoders.

## Slide 12: Thank You