## Slide 1
SMART AUTONOMOUS
MULTI-MODE ROBOT
USING ARDUINO
Project Report — Design, Block Diagram, Components & Working Principle
KLH — Front End Development Frameworks and UI Engineering (25CS1201E) | 2025-26, Term-III
Team Member | Roll Number
Samshritha | 2520030045
Lasya | 2520030538
Asritha | 2520030592
Bindhu | 2520030077
Lakshmi Sri | 2520030264

## Slide 2
Abstract
Overview of the system concept
Smart Autonomous Multi-Mode Robot Using Arduino is a mobile robotic system built to operate in both manual and autonomous modes.
An Arduino Uno acts as the main controller, processing commands and driving robot movement. A Bluetooth module lets a user control the robot wirelessly from a mobile device in manual mode. In autonomous mode, an ultrasonic sensor continuously scans for obstacles ahead, and the Arduino uses that data to make real-time movement decisions and avoid collisions.
Four gear motors, paired through an L293D motor driver, turn the robot wheels. Two Li-ion batteries power the system, and a physical switch turns the robot ON and OFF.
At a Glance
2
Operating modes — Manual (Bluetooth) & Autonomous
4
Gear motors driving 4 wheels
1
Ultrasonic sensor for obstacle avoidance
2
Li-ion batteries for portable power
Applications: surveillance · indoor navigation · educational robotics

## Slide 3
Block Diagram
Smart Autonomous Multi-Mode Robot Using Arduino
2x Li-ion Batteries
(7.4V pack)
ON / OFF
Switch
Vin / 5V
Bluetooth Module
(HC-05 / HC-06)
Arduino Uno
(Main Controller)
Ultrasonic Sensor
(HC-SR04)
Serial (Rx/Tx)
Trigger / Echo
IN1–IN4 (control)
L293D Motor Driver
(Dual H-Bridge)
Vs (motor supply)
Channel A
Channel B
Left Motors (2)
Channel A (parallel)
Right Motors (2)
Channel B (parallel)
Power path (7.4V / Vin / Vs)
Signal / control path

## Slide 4
Components & Specifications
Component | Qty | Spec | Function
Arduino Uno | 1 | ATmega328P, 5V logic | Main controller of the robot
Gear Motor | 4 | TT gear motor, 6–12V | Produces mechanical movement
Robot Wheel | 4 | 65–67 mm dia. | Provides movement on the surface
L293D Motor Driver | 1 | Dual H-Bridge, 600mA/ch | Controls motor direction & speed
Ultrasonic Sensor | 1 | HC-SR04, 2–400 cm range | Detects obstacles, measures distance
Bluetooth Module | 1 | HC-05 / HC-06, 9600 baud | Receives wireless commands
Li-ion Battery | 2 | 3.7V, 18650 cell | Provides power to the robot
Battery Holder | 1 | 2-cell holder | Holds the batteries
Jumper Wires | — | M-M / M-F | Electrical connections
Chassis (Dot Bot) | 1 | Acrylic/ABS platform | Mounting platform for components
Switch | 1 | SPST toggle | Turns the robot ON/OFF

## Slide 5
Working — Manual (Bluetooth) Mode
1
Power ON
Two Li-ion batteries power the system; the switch turns the robot ON.
2
Pair & Connect
The mobile phone connects to the HC-05/HC-06 Bluetooth module using a serial Bluetooth terminal app.
3
Send Command
The user sends a single character: F (forward), B (backward), L (left), R (right), or S (stop).
4
Arduino Decodes
The Bluetooth module relays the character to the Arduino Uno over serial (Rx/Tx).
5
Drive Motors
The Arduino sets the L293D's IN1–IN4 pins accordingly, and the motors turn the wheels in the commanded direction.
Command Reference
F
Forward
B
Backward
L
Left
R
Right
S
Stop
Protocol: HC-05/HC-06 serial module, 9600 baud, read via a mobile Bluetooth terminal app.

## Slide 6
Working — Autonomous Mode
No continuous user input required — the robot senses and reacts on its own.
Sensor pings: HC-SR04 sends ultrasonic pulse
Echo received → Arduino computes distance
Distance ≥ 15 cm ?
Yes
Continue moving forward
No
Stop motors (obstacle < 15 cm)
Reverse briefly (≈ 300 ms)
Turn right & re-scan with sensor
Resume forward scanning loop
Threshold example: if the measured distance falls below 15 cm, the Arduino stops the motors, reverses briefly (≈ 300 ms), turns right, then resumes scanning. Both the “Yes” and “No” paths loop back to sensor pinging, forming a continuous sense → decide → act cycle.

## Slide 7
Multi-Mode Operation
Mode selection: the Arduino checks for an incoming Bluetooth command first on each loop cycle; if none arrives within a short timeout, it falls back to autonomous obstacle-avoidance scanning.
Mode 1 — Bluetooth Controlled
Mobile Phone
Bluetooth Module
Arduino UNO
L293D Motor Driver
Motors → Robot Movement
Mode 2 — Autonomous
Ultrasonic Sensor
Obstacle Detection
Arduino UNO
Decision Making → L293D
Motors → Obstacle Avoidance

## Slide 8
Why Each Component Is Used
Arduino Uno
Processes sensor data and controls the entire robot.
L293D Driver
Arduino can't supply motor-level current directly, so this sits between Arduino and the motors.
Ultrasonic Sensor
Detects obstacles without physical contact.
Bluetooth Module
Provides wireless communication between phone and robot.
Gear Motors
Provide the torque needed to move the robot.
Robot Wheels
Convert motor rotation into robot movement.
Li-ion Batteries
Provide portable power — no wired supply needed.